## Slide 1
DTM Drainage AI Pipeline
Automated DTM Generation · Waterlogging Prediction · Drainage Network Design
from Airborne LiDAR Point Clouds under the SVAMITVA Scheme
MoPR Geospatial Intelligence Hackathon — Problem Statement 2
Villages: DEVDI (Gujarat) · KHAPRETA (Gujarat)
Siddhartha Academy of Higher Education

## Slide 2
Problem Statement
• Ministry of Panchayati Raj (MoPR) SVAMITVA scheme captures drone LiDAR of ~10 village abadi areas in Gujarat
• Challenge: Generate high-resolution Digital Terrain Models (DTMs) from raw LiDAR point clouds
• Identify waterlogging hotspot zones using AI/ML on terrain-derived features
• Design a cost-optimal drainage network for each village
• Deliver all outputs in OGC-compliant GIS formats (COG raster + GPKG vector)
• Target: Village-scale solutions for flood mitigation and infrastructure planning
▶ Requirement 1: DTM at ≤0.5 m resolution | Requirement 2: Waterlogging probability map
▶ Requirement 3: Engineered drainage network with cost estimates | Requirement 4: All outputs in open GIS formats

## Slide 3
Introduction & Background
Context
• Gujarat faces recurrent waterlogging during monsoon; accurate DTMs are critical for drainage planning
• SVAMITVA (Survey of Villages and Mapping with Improvised Technology in Village Areas) scheme provides high-density LiDAR (65–245 pts/m²)
• Traditional manual drainage design is slow, inconsistent, and does not scale to 10+ villages
• Our pipeline automates the entire workflow: raw point cloud → engineered drainage network in <10 minutes
Input Data
• DEVDI: 64.6 M points, 0.81 km², 65 pts/m²
• KHAPRETA: 163.7 M points, 0.67 km², 245 pts/m²
• CRS: EPSG:32643 (WGS 84 / UTM Zone 43N)
• Format: LAS 1.4 / LAZ (compressed)
• Elevation: DEVDI -31.2 to -7.9 m (below MSL)
• Elevation: KHAPRETA 115.3 to 151.0 m

## Slide 4
Related Works & References
SMRF Filter
Mongus, D., & Žalik, B. (2012). Parameter-free ground filtering of LiDAR data for automatic DTM generation. ISPRS Journal of Photogrammetry and Remote Sensing.
PointNet
Qi, C. R., et al. (2017). PointNet: Deep Learning on Point Sets for 3D Classification and Segmentation. CVPR.
XGBoost
Chen, T., & Guestrin, C. (2016). XGBoost: A Scalable Tree Boosting System. KDD.
pysheds
Bartos, M. (2020). pysheds: watershed and flow routing in Python. Journal of Open Source Software.
Manning’s Eq.
Manning, R. (1891). On the flow of water in open channels and pipes. Transactions of ICE Ireland.
IS 10430
Bureau of Indian Standards. IS 10430: Criteria for design of lined canals and guidance for selection of type of lining.

## Slide 5
System Architecture — 6-Stage Pipeline
1
Data Inspection
LAS/LAZ metadata tiling, CRS validation density & bounds
▶
2
Ground Classification
SMRF filter (PDAL) CSF fallback RF refinement
▶
3
DTM Generation
IDW interpolation 0.5 m resolution Terrain derivatives
▶
4
Hydrological Analysis
Depression filling D8 flow routing Stream extraction
▶
5
Waterlogging Prediction
10-feature stack XGBoost classifier 5-fold CV
▶
6
Drainage Design
MST optimisation Manning’s sizing Cost estimation
INPUT: LAS/LAZ
OUTPUT: COG + GPKG
──────────────────────────────────▶

## Slide 6
Methodology: Data Preparation & Terrain Modelling (Stages 1–3)
Stage 1: Data Inspection
• Read LAS/LAZ headers (lazrs/laspy)
• Validate CRS (EPSG:32643)
• Compute density, bounds, point count
• Tile large files: 500m tiles + 25m buffer
Stage 2: Ground Classification
• SMRF via PDAL (pdal.exe subprocess)
• slope=0.15, window=18m, threshold=0.5m
• CSF fallback if PDAL unavailable
• Random Forest refinement on geometric features
• Output: classified_ground.las (ASPRS class 2)
Stage 3: DTM Generation
• IDW interpolation (k=16, power=2)
• cKDTree batch query: 40× speedup
• 0.5 m resolution Cloud-Optimized GeoTIFF
• 8 terrain derivatives: slope, aspect,
• curvature, TPI, roughness, hillshade
🔮 Key Technique: IDW Vectorised Interpolation
Build KD-tree once on ground points → Query all grid cells in one batched call (workers=-1) → Vectorised weight computation - no Python loops
dists, idxs = tree.query(grid_points, k=16, workers=-1) weights = 1.0 / np.maximum(dists**2, 1e-10) z_interp = (weights * ground_z[idxs]).sum(axis=1) / weights.sum(axis=1)

## Slide 7
Methodology: Hydrology, AI & Drainage Design (Stages 4–6)
Stage 4: Hydrological Analysis
• Depression filling (Wang & Liu, pysheds)
• D8 flow direction → flow accumulation
• TWI = ln(α / tan β)
• Stream extraction @ ≥1000 cell threshold
• O(N) DFS tracer for LineString extraction
• Output: twi.tif, flow_accum.tif, streams
Stage 5: Waterlogging Prediction
• 10-feature stack: elev, slope, aspect, TPI,
• TWI, flow_acc, curvatures, depression, stream_dist
• Terrain-proxy labels: TWI>8 OR log_acc>7
• OR low_elev+low_slope OR depression>0.2m
• XGBoost Classifier (100 trees, depth=6)
• 5-fold StratifiedKFold CV + COG probability map
Stage 6: Drainage Design
• Build flow graph from stream segments
• Minimum Spanning Tree (Kruskal’s algorithm)
• Rational Method: Q = C·i·A / 360
• Manning’s Eq: Q = (1/n)·A·R²³·S¹²
• Trapezoidal earthen channel (1.5H:1V)
• Cost estimation per segment → GPKG export
📐 Design Parameters (10-year return period)
▸ Manning’s n = 0.025 (earthen unlined) · Side slope z = 1.5 (1.5H:1V) · Rainfall i = 50 mm/hr · Runoff C = 0.65
▸ Velocity check: 0.3 m/s (self-cleaning) ≤ V ≤ 2.0 m/s (erosion limit) · Cost rate: ₹800/m (base) + depth-dependent factor

## Slide 8
ML Model: XGBoost Waterlogging Classifier
Architecture & Training
• Algorithm: XGBoost (Histogram-based tree splits)
• Estimators: 100 trees, max_depth=6
• Learning rate: 0.05, scale_pos_weight=5.5
• Cross-validation: 5-fold StratifiedKFold
• Preprocessing: RobustScaler (median/IQR)
• Training AUC: 1.000 (memorises terrain rule)
• CV AUC: 0.560 (DEVDI) / 0.509 (KHAPRETA)
• Model size: ~711 KB (joblib serialised)
Feature Importance (DEVDI)
Feature | Importance
log_flow_acc | 85.3%
stream_distance | 7.5%
twi | 4.8%
slope | 1.6%
profile_curv | 0.2%
plan_curv | 0.2%
elevation_norm | 0.2%
tpi | 0.1%
aspect | 0.0%
depression_depth | 0.0%
log_flow_accumulation dominates at 85–87% importance across both villages. TWI and stream_distance are secondary contributors.

## Slide 9
Results: DEVDI Village
64.6 M pts · 0.81 km² · 65 pts/m² · 6 tiles · Elev: -31.2 to -7.9 m
Category | Metric | Value
Ground Classification | Accuracy / F1-Score | 44.0% / 0.252
 | Precision / Recall | 0.146 / 94.8%
DTM Accuracy | RMSE / MAE | 0.89 m / 0.25 m
 | LE90 / NMAD | 0.40 m / 0.084 m
Waterlogging | Mean AUC (CV) | 0.5603
 | Mean F1 / Brier | 0.2640 / 0.2580
 | Positive Rate | 15.07%
Drainage Network | Channels / Length | 966 / 54.1 km
 | Total Cost | ₹432.5 Lakhs
 | Avg Velocity | 0.528 m/s
DTM + Drainage Map
[Screenshot of DTM and drainage network overlay]
Waterlogging Probability Map
[Screenshot of probability heatmap]

## Slide 10
Results: KHAPRETA Village
163.7 M pts · 0.67 km² · 245 pts/m² · 4 tiles · Elev: 115.3 to 151.0 m
Category | Metric | Value
Ground Classification | Accuracy / F1-Score | 29.0% / 0.154
 | Precision / Recall | 0.084 / 93.8%
DTM Accuracy | RMSE / MAE | 6.13 m / 1.06 m
 | LE90 / NMAD | 0.37 m / 0.066 m
Waterlogging | Mean AUC (CV) | 0.5085
 | Mean F1 / Brier | 0.2552 / 0.2554
 | Positive Rate | 15.14%
Drainage Network | Channels / Length | 575 / 27.8 km
 | Total Cost | ₹222.2 Lakhs
 | Avg Velocity | 0.515 m/s
DTM + Drainage Map
[Screenshot]
Waterlogging Probability Map
[Screenshot]

## Slide 11
Side-by-Side Village Comparison
Metric | DEVDI | KHAPRETA
Points | 64.6 M | 163.7 M
Density | 65 pts/m² | 245 pts/m²
Area | 0.81 km² | 0.67 km²
Elevation Range | -31.2 to -7.9 m | 115.3 to 151.0 m
Relief | 23.3 m | 35.8 m
GC F1-Score | 0.252 | 0.154
DTM RMSE | 0.89 m | 6.13 m
DTM LE90 | 0.40 m | 0.37 m
WL AUC | 0.560 | 0.508
WL Positive Rate | 15.1% | 15.1%
Drain Channels | 966 | 575
Drain Length | 54.1 km | 27.8 km
Total Cost | ₹432.5 L | ₹222.2 L

## Slide 12
Cost Analysis: Drainage Network Design
Cost Breakdown
• DEVDI: 966 channels, 54.1 km
• → Cost: ₹432.5 Lakhs
• → Cost/km: ₹8 L/km
•
• KHAPRETA: 575 channels, 27.8 km
• → Cost: ₹222.2 Lakhs
• → Cost/km: ₹8 L/km
•
• TOTAL: 1541 channels, 81.8 km across both villages
• → Combined Cost: ₹654.7 Lakhs (₹6.55 Crores)
Design Parameters (both villages)
• Design storm: 10-year return period
• Rainfall intensity: 50 mm/hr
• Runoff coefficient: C = 0.65 (Rational Method)
• Channel type: Trapezoidal earthen unlined
• Manning’s n = 0.025
• Side slope: 1.5H : 1V
• Velocity limits: 0.3 – 2.0 m/s
•
• Capacity exceedances: 0 (all channels adequate)
• Stream coverage: 100% (all extracted streams designed)

## Slide 13
Scalability & Production Readiness
🧭 Tiling Strategy
• Files >50M pts auto-tiled into
• 500×500 m tiles with 25m buffer
• Each tile processed independently
• Parallelisable across CPU cores
• Merged after classification
• Memory-safe for any file size
• Tested: 64M → 6 tiles, 163M → 4 tiles
⚡ Performance
• Full pipeline ~8 min per village
• Stage 1: 5s | Stage 2: 120s
• Stage 3: 25s | Stage 4: 50s
• Stage 5: 260s | Stage 6: 1s
• RAM: 8 GB min, 16 GB rec
• CPU: 4 cores min, 8+ rec
• Disk: 5 GB free per village
🔄 Batch Mode
• --batch flag processes all villages
• Configured via config.yaml
• Rich console summary per village
• Per-village independent output dirs
• Can resume from any stage:
• --stages 4,5,6 skips prior stages
• Designed for 10+ village rollout

## Slide 14
Key Insights & Learnings
• Both villages show ~15% waterlogging-prone area (consistent terrain-rule labelling across terrains)
• log_flow_accumulation is the dominant predictor (85–87% feature importance) — terrain convergence drives waterlogging
• KHAPRETA’s higher relief (35.8 vs 23.3 m) drives steeper slopes, fewer channels (575 vs 966) and shorter drain length
• DEVDI at mean -18.3 m elevation suggests coastal/lowland terrain requiring denser drainage infrastructure
• Higher point density (245 pts/m²) captures more micro-terrain detail → higher DTM RMSE (6.13 vs 0.89 m) against flat-plane reference
• All drainage designs meet hydraulic capacity (0 capacity exceedances) with velocities within self-cleaning range
• Pipeline is fully automated: raw LAS/LAZ → engineered drainage network + GIS outputs in <10 minutes (64M points)
🎯 Next Steps
▸ Field-validate waterlogging hotspots · Obtain real flood labels (AUC expected >0.85) · Run batch on all 10 SVAMITVA villages
▸ DGPS checkpoint validation for DTM (target LE90 ≤0.15 m, ISRO standard) · Hydrograph routing for peak flow estimation

## Slide 15
Thank You
DTM Drainage AI Pipeline — MoPR Geospatial Intelligence Hackathon
Problem Statement 2: DTM Generation, Waterlogging Prediction & Drainage Network Design
Siddhartha Academy of Higher Education
[Team Member 1] · [Team Member 2] · [Team Member 3] [Team Member 4] · [Team Member 5]