## Slide 1
DTM Drainage AI Pipeline
Automated DTM Generation, Waterlogging Prediction & Drainage Network Design from LiDAR Point Clouds
SVAMITVA Scheme — Ministry of Panchayati Raj | MoPR Geospatial Intelligence Hackathon
Villages Processed: DEVDI (Gujarat) • KHAPRETA (Gujarat)

## Slide 2
Pipeline Overview
Stage 1
Data Inspection
LAS/LAZ tiling, density & bounds
Stage 2
Ground Classification
SMRF filter (PDAL) → ground/non-ground
Stage 3
DTM Generation
IDW interpolation → 0.5 m COG + terrain derivatives
Stage 4
Hydrological Analysis
Fill → D8 flow → accumulation → TWI → streams
Stage 5
Waterlogging Prediction
XGBoost on 10 terrain features
Stage 6
Drainage Design
MST optimisation + Manning’s hydraulic sizing

## Slide 3
DEVDI
64.6 M points • 0.81 km² • 65 pts/m² • 6 tiles
DTM Drainage AI Pipeline — MoPR Geospatial Hackathon

## Slide 4
DEVDI — Pipeline Results
Metric | Value
Ground Classification | Acc=43.99%, F1=0.252, Rec=94.75%
DTM Accuracy | RMSE=0.89m, MAE=0.25m, LE90=0.40m
DTM Elevation Range | -31.2 to -7.9 m (mean: -18.3 m)
Waterlogging Model | AUC=0.560, F1=0.264, Brier=0.258
Waterlogging Hotspots | 402,191 / 2,628,935 cells (15.3%)
Drainage Network | 966 channels, 54.1 km, ₹432.5L
Avg Flow Velocity | 0.53 m/s

## Slide 5
DEVDI — Drainage Network Design
Parameter | Value
Total Channel Segments | 966
Total Channel Length | 54.06 km
Estimated Construction Cost | ₹432.51 Lakhs
Avg Design Velocity | 0.528 m/s
Capacity Exceedances | 0
Stream Coverage | 100%
Top features: log_flow_acc (85.3%), stream_distance (7.5%), twi (4.8%)

## Slide 6
KHAPRETA
163.7 M points • 0.67 km² • 245 pts/m² • 4 tiles
DTM Drainage AI Pipeline — MoPR Geospatial Hackathon

## Slide 7
KHAPRETA — Pipeline Results
Metric | Value
Ground Classification | Acc=28.96%, F1=0.154, Rec=93.82%
DTM Accuracy | RMSE=6.13m, MAE=1.06m, LE90=0.37m
DTM Elevation Range | 115.3 to 151.0 m (mean: 133.8 m)
Waterlogging Model | AUC=0.508, F1=0.255, Brier=0.255
Waterlogging Hotspots | 271,606 / 1,809,138 cells (15.0%)
Drainage Network | 575 channels, 27.8 km, ₹222.2L
Avg Flow Velocity | 0.52 m/s

## Slide 8
KHAPRETA — Drainage Network Design
Parameter | Value
Total Channel Segments | 575
Total Channel Length | 27.78 km
Estimated Construction Cost | ₹222.22 Lakhs
Avg Design Velocity | 0.515 m/s
Capacity Exceedances | 0
Stream Coverage | 100%
Top features: log_flow_acc (87.2%), stream_distance (5.5%), twi (3.9%)

## Slide 9
Village Comparison Summary
Metric | DEVDI | KHAPRETA
Area | 0.81 km² | 0.67 km²
Point Density | 65 pts/m² | 245 pts/m²
DTM RMSE | 0.89 m | 6.13 m
DTM LE90 | 0.40 m | 0.37 m
DTM Relief | 23.3 m | 35.8 m
Channels | 966 | 575
Drain Length | 54.1 km | 27.8 km
Total Cost | ₹432.5 L | ₹222.2 L
WL AUC | 0.560 | 0.509
WL Pos Rate | 15.3% | 15.0%

## Slide 10
Key Insights & Next Steps
Both villages show ~15% waterlogging-prone area (consistent terrain-rule labelling)
log_flow_accumulation is the dominant predictor (85–87% importance)
KHAPRETA’s higher relief (35.8 m vs 23.3 m) drives steeper slopes and fewer channels (575 vs 966)
DEVDI has lower elevation (mean -18.3 m) suggesting coastal/lowland terrain with denser drainage
KHAPRETA’s higher point density (245 vs 65 pts/m²) gives higher DTM RMSE due to more terrain detail
All drainage designs meet hydraulic capacity (0 capacity exceedances)
Next: field validation of waterlogging hotspots, integration with rainfall-runoff models