## Slide 1
DTM Drainage AI
Automated Terrain Modelling · Waterlogging Risk · Drainage Network Design
End-to-end pipeline from airborne LiDAR point clouds — SVAMITVA scheme
MoPR Geospatial Intelligence Hackathon · Problem Statement 2
Team: charansaiponnada · IIT Tirupati
4 villages processed across Gujarat & Punjab · Devdi Khapreta Dhal Hoshiarpur Chakhirasingh
Raw LiDAR → DTM + Risk Map + Costed Drainage in one automated run

## Slide 2
The Problem
Rural India needs scalable, data-driven flood-mitigation planning
• MoPR's SVAMITVA scheme captures drone LiDAR over thousands of village abadi areas — a vast, underused 3-D terrain asset.
• Manual drainage planning is slow, inconsistent, and cannot scale to 600,000+ villages.
• Monsoon waterlogging damages property and health; planners lack objective, repeatable hotspot maps.
• Raw point clouds are not directly usable — they must be turned into terrain models, risk maps and engineered designs.
# | Deliverable required by PS-2
1 | High-resolution Digital Terrain Model (≤0.5 m) from raw LiDAR
2 | AI/ML waterlogging risk map over terrain-derived features
3 | Cost-optimised drainage network with hydraulic design
4 | All outputs in open OGC formats (COG raster + GeoPackage vector)

## Slide 3
Our Solution — One Automated Pipeline
Raw LAS/LAZ in · OGC-compliant DTM, risk map and costed drainage out
Fully automated
• Single command runs all 6 stages
• No manual GIS steps
• Batch mode for many villages
Physically grounded
• SMRF ground filter + IDW DTM
• D8 hydrology, TWI, depressions
• Manning's hydraulics + costing
Scalable & open
• Auto-tiling for any file size
• Cloud-Optimized GeoTIFF + GPKG
• Transfers across states
4
villages, 2 states
314M
LiDAR points processed
135 km
drainage designed
₹1097L
costed network

## Slide 4
System Architecture — 6-Stage Pipeline
One command · raw LiDAR in → OGC-compliant DTM, risk map and costed drainage out
1
Inspect
• LAS/LAZ metadata
• Auto-tiling
• CRS validation
laspy · numpy
▶
2
Classify
• SMRF filter (PDAL)
• RF refinement
• ASPRS class-2
pdal · sklearn
▶
3
DTM
• IDW (cKDTree)
• 0.5 m COG
• 8 derivatives
scipy · rio-cogeo
▶
4
Hydrology
• Depression fill
• D8 + TWI
• Stream extract
pysheds
▶
5
Waterlogging
• 10-feature stack
• XGBoost surrogate
• CV + transfer
xgboost
▶
6
Drainage
• MST routing
• Manning's sizing
• Cost → GPKG
networkx
INPUT · LAS / LAZ
OUTPUT · COG + GPKG
──────────── 6 automated stages ────────────

## Slide 5
Methodology — Terrain Modelling (Stages 1–3)
1 · Inspect
• Read LAS/LAZ headers (laspy)
• Validate CRS, density, bounds
• Auto-tile big files (200 m + 25 m buffer)
2 · Classify
• SMRF morphological filter (PDAL)
• Random-Forest refinement
• Output ASPRS class-2 ground LAS
3 · DTM
• IDW interpolation (cKDTree, k=16)
• 0.5 m Cloud-Optimized GeoTIFF
• 8 terrain derivatives computed
Terrain derivatives from the DTM: slope · Topographic Wetness Index · hillshade

## Slide 6
Methodology — Hydrology, AI & Drainage (Stages 4–6)
4 · Hydrology
• Depression filling (pysheds)
• D8 flow direction + accumulation
• TWI = ln(α / tan β)
• Stream network extraction
5 · Waterlogging
• 10-feature terrain stack
• XGBoost risk surrogate
• Physically-grounded risk index
• 5-fold CV + cross-village test
6 · Drainage
• Minimum Spanning Tree routing
• Rational method: Q = C·i·A/360
• Manning's trapezoidal sizing
• Per-segment cost → GeoPackage
Drainage design parameters (10-year return period)
▸ Manning's n = 0.025 (earthen) · side slope 1.5H:1V · rainfall i = 50 mm/hr · runoff C = 0.65
▸ Velocity window 0.3–2.0 m/s (self-cleaning, non-erosive) · cost rate depth-dependent per metre
▸ Every channel sized to carry its catchment's design discharge — zero capacity exceedances

## Slide 7
How We Validate — Honest, Defensible Metrics
No fabricated accuracy: every number comes from a withheld or independent check
Output | Validation method | Why it is defensible
DTM accuracy | Leave-out cross-validation: interpolate withheld LiDAR ground returns and compare | True vertical error vs real measurements — ASPRS-style, not a self-comparison
Waterlogging | 5-fold CV fidelity to a physically-derived risk index + cross-village transfer | Tests genuine generalisation across terrain, not memorised thresholds
Drainage | Hydraulic capacity check (Manning's) on every designed channel | Engineering constraint satisfaction, fully reproducible
Transparent about limits
• No observed flood records exist for these villages, so waterlogging labels are physically-derived, not ground-truthed — we report this openly.
• DTM has no external survey reference; we validate internally against the LiDAR returns themselves (the densest available truth).

## Slide 8
Results — DTM Vertical Accuracy
Leave-out cross-validation against withheld LiDAR ground returns
Key takeaways
• RMSE 0.10–0.25 m across villages
• LE90 (ASPRS) as low as 0.13 m
• Decimetre-level fit on dense terrain
• Errors track relief: flatter abadi areas are most accurate
• Same IDW method validated identically on every village

## Slide 9
Results — Waterlogging Risk & Cross-Village Transfer
The honest generalisation test: train on one village, predict another
Strong off-diagonal AUC shows the model learns transferable terrain→risk structure, not village-specific thresholds. Next step: calibrate against observed flood events.

## Slide 10
Per-Village Results — Drainage & Hotspots
Devdi · Gujarat
DTM RMSE 0.1762 m · LE90 0.2349 m · WL AUC 0.9993 966 channels · 54.1 km · ₹434 L
Khapreta · Gujarat
DTM RMSE 0.1458 m · LE90 0.1914 m · WL AUC 0.9999 575 channels · 27.8 km · ₹233 L

## Slide 11
Per-Village Results — Drainage & Hotspots
Dhal Hoshiarpur · Punjab
DTM RMSE 0.0969 m · LE90 0.1289 m · WL AUC 0.9994 297 channels · 9.8 km · ₹79 L
Chakhirasingh · Punjab
DTM RMSE 0.2544 m · LE90 0.3851 m · WL AUC 0.9989 1013 channels · 43.7 km · ₹351 L

## Slide 12
Results Scorecard — All Villages
One pipeline, one config — identical processing and validation applied to every village across two states.

## Slide 13
Drainage Network Design — Worked Example
Devdi: MST-routed, hydraulically-sized, fully costed
Design summary
Metric | Value
Channels | 966
Total length | 54.1 km
Total cost | ₹434 Lakh
Avg velocity | 0.543 m/s
Capacity fails | 0
Channels follow natural flow paths (minimum spanning tree), each sized by Manning's equation to carry its catchment's 10-yr design storm.

## Slide 14
Scalability & Production Readiness
Handles any size
• Auto-tiling with overlap buffer
• Chunked streaming I/O
• Tested up to 170 M+ points
• Memory-safe on commodity hardware
Transfers across regions
• Validated in Gujarat & Punjab
• Cross-village model transfer shown
• One config, many villages
• No per-site manual tuning
Open & integrable
• Cloud-Optimized GeoTIFF rasters
• GeoPackage vector layers
• Loads directly in QGIS/ArcGIS
• OGC-compliant for govt GIS

## Slide 15
Limitations & Roadmap
What we would do with more data and time — stated plainly
Current limitations
• Waterlogging labels are physically-derived, not yet validated against observed floods.
• DTM lacks an independent DGPS survey reference; validated against the LiDAR returns.
• Ground-refinement gains over SMRF are marginal on flat abadi terrain.
• 4 villages processed; pipeline is ready to run on the remaining SVAMITVA tiles.
Roadmap
• Calibrate risk model on real flood-event / drain-complaint records (expected AUC ↑).
• DGPS checkpoints for absolute DTM accuracy (target LE90 ≤ 0.15 m).
• Roll the batch pipeline across all 10 villages and beyond.
• Add rainfall-runoff hydrograph routing for peak-flow design.
• Web dashboard for planners to inspect and edit networks.

## Slide 16
Thank You
DTM Drainage AI — MoPR Geospatial Intelligence Hackathon
charansaiponnada · IIT Tirupati
Automated DTM · Waterlogging Risk · Drainage Design from LiDAR point clouds
Built end-to-end · Validated honestly · Ready to scale